## Slide 1: Wine Production

## Slide 2: Defining the term
Wine is an alcoholic beverage made by the fermentation of grape juice or other sugar-containing substrates including honey, sugarcane, fruit juices, and other plant juices containing sugars such as palm tree sap, floral extracts, and Agave, the century cactus plant.
Wine is distinguished from beer, in which the fermentable sugars are derived principally from starches by means of amylases produced in cereal grains, particularly barley, by germination or malting.

## Slide 3: Microorganisms
The principal microorganisms in the alcoholic fermentation of wines are yeasts belonging to genus Saccharomyces, in particular S. cerevisiae, S. cerevisiae var. ellipsoideus, S. bayanus, and S. oviformis.
Although yeasts belonging to genus Saccharomyces are generally present in the grapes or other fruits and they are capable of fermenting the juice to wine, it is a generally accepted procedure, particularly in wine companies, to inoculate pure cultures of selected wine yeasts.
These may be selected for flavor, production of little or no foam, ability to ferment at low temperatures, or flocculation–sedimentation behavior. They are more often selected for the absence of any undesirable flavors in wines.

## Slide 4
Another group of microorganisms accompanying the yeast in wine fermentations is the lactic acid bacteria.
Grape juice contains mainly tartaric acid and malic acid. If the acidity is too high for the best flavor, it may be desirable for lactic acid bacteria to ferment the malic to lactic acid, which decreases the total acidity and raises the pH of the wine.

## Slide 5: Metabolism
S. cerevisiae and other wine yeasts have the ability to grow and metabolize sugars, such as glucose, fructose, and sucrose, aerobically or anaerobically.
Aerobic growth yields far more energy and the yeasts multiply vigorously, but little if any ethanol is produced.
Anaerobically, yeasts dissimilate glucose according to the Emden–Meyerhof scheme.
Theoretically, 1 mol (180 g) of glucose yields 2 mol (92 g) of ethanol and 2 mol (88 g) of carbon dioxide.
Actually, yields are slightly less because of the production of glycerol and other minor compounds

## Slide 6: Wine Classification
Wines are classified according to color (white, red, or rose/pink) and how much ethanol they contain.
Wines with 7–14% ethanol are described as table wines; more than 14% ethanol designates fortified wines, such as port and sherry.
Wines are dry (nonsweet), semidry, semisweet, or sweet.
Still wines given a secondary fermentation in the bottle or in a tank to produce carbon dioxide under pressure are called ‘sparkling’.
Wines are also designated, at times, by the type of grape from which they have been made.

## Slide 7: Steps in Manufacture of Wine
Harvesting
  Grapes should be harvested when they are at their peak of maturity and desired flavor with a high sugar content and desirable acidity. They should be as intact as possible and be processed quickly.
  For white wines, the stems are removed and the grapes are crushed.
  The skins are retained for red wines.
  Pectinase may be added to facilitate juice extraction.

## Slide 8
Fermentation
  Fermentation can proceed either through the action of the naturally present yeast or by the inoculation of a selected pure yeast culture.
Fermentation temperature
  10–15 °C for white wines and somewhat higher for red wines.
  The higher the temperature, up to about 30 °C, the more rapid the fermentation;
  however, the slower, lower temperature fermentations are considered to lead to higher-quality wines because less volatile aroma is lost.

## Slide 9
The Sugar Content
  about 13% w/v to yield a 7% v/v alcohol wine
  about 22% to yield a 12% v/v alcohol wine.
  The sugar content of the juice may be raised before or during fermentation to adjust the final ethanol content.
  A weight of carbon dioxide gas almost equivalent to the weight of ethanol produced is released during fermentation. This causes the fermentation to ‘boil’ during its most active phases.

## Slide 10
Racking
As the fermentation nears completion, the yeast cells tend to settle, and after fermentation has been completed, the wine can be decanted or siphoned (racked) as the first step in clarification of the wine.
This may be combined with cold stabilization, which is accomplished by storing the wine at about 2 °C.
Cold stabilization removes excess tartrates and other materials that might cause cloudiness in the bottle later.

## Slide 11
Clarification
  Most wine consumers like a crystal-clear wine with no haze or sediment.
  To accomplish this objective, gelatin, isinglass, or egg white may be added to the wine.
  These ingredients combine with tannin and form a fine precipitate that removes some of the materials that might cause turbidity.
  White wines may not contain sufficient tannin. In that case, some added tannin sufficient to react with the added protein may be necessary to produce the precipitate and stabilize the wine.
  Bentonite, a clay, is also widely used for clarification.

## Slide 12
Bottling
  Wines are generally bottled in dark green or brown bottles to decrease the deleterious effects on quality that can be caused by sunlight.
  Small amounts of sulfite may be added to inhibit oxidation.
  Sweet wines may be fortified with ethanol (18–20%) or the wines may be pasteurized or sterile-filtered (the choice for high-quality wines) to prevent the growth of contaminants in the bottle.

## Slide 13
Aging
  Aging occurs after fermentation. It can occur in tanks, in barrels, or in the bottle.
  The flavor may be improved through esterification reactions in which small portions of ethanol combine with organic acids in the wine.
  Aging improves some wines, but has little effect on others.